Hex Vex Assembly Reference
xasm assembly type 1
Version 1 - 17/06/2019

# About
HexVex is a simple and primitive computer architecture. Not a true 16 bit system, yet capable of handling 16 bit numbers in single instructions, depending on needs.
It is designed to be used with the same 16 bit address × 8 bit data ROMs for program memory and decoders.
It doesn't use a RAM, but one might be used in place of the ROM for program memory, if so preferred.
NOTES:
Mention the state flags/indicators.
NOTES:
- The pwm and halt opcodes are still untested.
- System interruption support needs testing.
- The poke and tell opcodes have been added along with a special signalling wire for peripherals that take setup codes.
# Terminology notes
Some terms used in this document are used differently from what might be usually expected for other computer architectures.
Ticks	1 Tick is one clock cycle period.
Cycles	1 Cycle is the number of clock cycles to execute an instruction.
Program Memory	The device where instructions are loaded from.
Store	How it's referred to the pair composed of the Main Bus and Auxiliary Bus. Together they can transport a 16 bit number or 2 8bit numbers being used independently.
Cache	Two internal 8bit registers, each overwatching each Store bus. They can be used as intermediaries when transposing numbers to multiple registers.
Pointer	Address given to the program memory. It is usually referring to the address of the first byte starting an instruction.

# Conditions to test against
Every instruction is started with a conditional flag, which is used by the computer to check against some flag of the internal state register. If the flag is matched, the instruction is accepted and executed.
Mnemonic	Hex	Description
_	0x00	This instruction will always be accepted in ANY case
:	0x01	CARRY flag is raised
+	0x02	Bool is TRUE (since last time the flag was set)
-	0x03	Bool is FALSE (since last time the flag was set)
!	0x04	Numbers are DIFFERENT (since last comparison)
>	0x05	Number is GREATER than Accumulator value (since last comparison)
<	0x06	Number is LESSER than Accumulator value (since last comparison)
=	0x07	Numbers are EQUAL (since last comparison)

# Assembler Specific Symbols
When programming by writing for the assembler, other symbols may be in place of conditional flags, but don't make functional instructions. They convey meaning only to the assembler.
Check example programs to learn how to use them.
#	A comment. The line starting with this symbol will be completely ignored.
|	An import. The assembler will read a program from another file and place it in the line this symbol appears. The text after this symbol is the file path.
*	A variable declaration. If an instruction argument isn't a number, the assembler will look for lines with this symbol for a match and use the associated number in place.

## The Case of «[label]»
Strings enclosed in square brackets mark a position which pointer can be referenced as a variable. This is similar to "labels" for jumping in other programming languages, and enables a mechanism for subroutines.
System interrupts will trigger special labels and even if not used, they should be written in the program to avoid unexpected behaviour. It's advised that all programs end with a halting instruction. So that runaway code, including unused interrupts don't cause pointer overflow or other oddities. The make it easier to the programmer, such recommendations are already accounted for in the «defaults.xasm» file, if available.

# Operation Codes
The conditional flag leads the opcode, which tells the action to perform with the arguments. One of the letters of a mnemonic might suggest how the computer will be interpreting the arguments.
n	number is a LITERAL INTEGER (8b or 16b depending on particular opcode)
r	number is a REGISTER ADDRESS
c	number is taken from the internal CACHE (always 16b)

Mnemonic	Hex	Argument 1	Argument 2	Description
nhalt	0x00	16 bit int		Stop executing. If argument > 0x0, then just sleep for n-16b ticks.
rhalt	0x01	address		Stop executing. Take sleep duration from a register
chalt	0x02	None		Stop executing. Take sleep duration from cache
ravn	0x03	None		Halt and Catch Fire. Prompts all addresses and writes their number into them, sequentially
poke	0x4	address		Send auxiliary signal for address to receive.
tell	0x5	address	8 bit int	Setup device at address with the given setup pattern.
ngoto	0x08	16 bit int		Jump to pointer given
rgoto	0x09	address		Jump to pointer taken from register
cgoto	0x0a	None		Jump to pointer stored in cache
cont	0x0b	16 bit int		Return to the pointer that was left off since last interruption, plus some offset from the arguments
gobak	0x0c	16 bit int		Return to the pointer where the last jump was performed, plus some offset from the arguments
rept	0x0d	16 bit int		Repeat pointer of current instruction, plus some offset
nmove	0x10	8 bit int	address	Write given integer to the register with given address
rmove	0x11	address	address	Copy value of one register to another
accfet	0x12	None		Copy value in the Accumulator to the cache
hexfet	0x13	16 bit int		Write given integer into the cache
utfet	0x14	None		Copy value in the User Timer into the cache
xfeed	0x15	address		Swap the value of register and the accumulator
!t	0x24	None		Toggle the state of the User Timer
t>n	0x25	16 bit int		Start counting from the given integer
t>r	0x26	address		Start counting from the value from a given register
t>c	0x27	None		Start counting from the value stored in the cache
t+n	0x28	16 bit int		Load User Timer with given integer, but keep state
t+r	0x29	address		Load User timer with value from given register, but keep state
t+c	0x2a	None		Load User Timer with value from cache, but keep state
pwm	0x2b	8 bit int	8 bit int	Set the high and low state period then use User Timer to generate pulse width modulation.

# Assembling Instructions
Each instruction is composed of 4 pointers in the program memory. The first pointer is a byte for control and it's composed of the conditional flag number (3 bits) concatenated to the opcode number (5 bits).
Example:
+nmove ➙ 0x02_0x10 ➙ 0b010_0b10000 ➙ 0b01010000

The second and third bytes are arguments to the opcode. Whatever they mean depends on a particular opcode.
The instruction is executed when the 4th byte is pointed to, but the value of that byte isn't processed by the computer.
The following example instruction will move the number 0x42 (decimal 66) to a register in the location 0xf1 if, and only if, the Boolean flag is positive:
+nmove 0x42 0xf1 ➙ 01010000 01000010 11110001 00000000

# Registers & Arithmetic & Logic Functions
Hex Vex is designed to be modular, with any general purpose registers being connected to the exposed Store and Address buses. The address to which each responds to is completely set by the programmer by some physical mechanism in the module, like DIP switches. Internal registers are either addressed by direct wiring from the control unit or also DIP switches set up by the programmer. It's advised to import the addresses from «defaults.xasm» when in doubt.
The ALU is composed of an internal Accumulator register which reads from its dedicated Bus. The ALU bus is exposed so that ALU modules can be connected.
Each ALU function is treated like a general purpose register and thus written to by the same addressing system as other registers. Each time something is written into an ALU module, the operation is automatically performed and stored in the accumulator.
All ALU operations are performed with the Accumulator value as one of the operands.
It isn't possible to read from ALU modules for obvious reasons, so the Accumulator should be addressed for reading instead. Some opcodes take the whole 16bit number from the Accumulator, but you can also supply addresses for individual halves of the Accumulator number.
The cache works in a similar way in that you can read from either of each half individually.
The addresses for any of these components will be specified in the file "defaults.xasm" if supplied.
# Peripheral Setup Function
NOTES: specify if “input/output device” means “into” or “from” bus.
Some devices may have the benefit of being setup to respond differently to data being written into them or behave in some special way when queried for reading. For example, a GPIO which has an interface to interact with the external world can be set to output a value to its pins or be set to take input from some sensor. For this, the device is connected to the “periphlag” wire which signals the device to change its setup state, and also the Auxiliary Bus from which the setup pattern is taken. Whatever this setup pattern does will depend on the device receiving it. The standard GPIO device, for example, takes the first bit to know whether its mode state is to be toggled (thus become an input device if it’s an output and vice-versa) in case of «0», or if it’s mode is to be set specifically to what the second bit tells it to be, «1» making it an input device, «0» being an output device.
# Design Details and Tips
0 – From this page forward the document really needs more TLC. It’s still a work in progress.
1 – As per revision of HexVex at the time of writing this note isn't true but it is planned for implementation: Any instruction that couldn't be decoded by the computer, will be gracefully skipped, taking only 1 tick from the system cycle instead of the usual 4.
2 – Under current iteration of the architecture there isn’t an ALU module which changes the boolean internal flags. The number comparator will write to all the 4 “comparison” flags at once instead. So the purpose of the Boolean conditional flags is to allow provisions for possible future features or streamlining. If you make your own ALU module, like a custom number comparator which writes to Bool instead, you might appreciate this provision.
3 - In a pursuit of reducing the number of instructions overall and keep the amount of instructions even, regardless of mathematical complexity, the ALU works like a mathematical integration function. For each ALU prompt, the Accumulator feeds its Least Significant Bits into the Auxiliary Bus and the where they are picked up by the ALU modules, along with whatever's present in the Main Bus. The result is then stored back into the Accumulator, thus effectively, the Accumulator is in a feedback loop and addresses for function modules pick the desired feedback network. At any moment, the accumulator value can be retrieved into the cache enabling multiple operation to be performed without interference. You can think of HexVex as a digital equivalent to an Operational Amplifier, given the right ALU modules and choice of instructions.
4 - Clearing the Accumulator can be performed by multiplying by zero. Loading a specific number can then be done by addition.
5 - The "nhalt" instruction with the "any" flag are chosen to result in the 0b0 code as a safety for the possibility of the computer to run into empty program memory lines, thus avoiding pointer overflow. So, in such situation, the computer will gracefully stop executing.
6 - Timer codes control the "User Timer" which is dedicated to be used by the programmer for whatever. You can count how many ticks it takes to execute an algorithm, for example.
7 - HexVex was designed to be relatively easy to remember the machine language codes and thus enable programming without an assembler. The choice of the binary numbers associated with each action is such as to enable heuristical/intuitive thinking about the instruction set.
You could pretend there are only 4 opcodes: Execution, Goto, Move and Timer. Thus, 2 of the 5 bits for opcode specify which of these: 0b00, 0b01, 0b10 and 0b11. The 3 bits left specify a modifier of the these four functions: 0b000, 0b001, 0b010, 0b011, 0b100, etc... if modifier is available. You could think as the 2 first bits as specifying which action to perform and the last 3 bits as specifying how to interpret the arguments. The conditional flags are similar: 0b000 it doesn't care about flags, 0b001 it kinda cares; it's usually rejected. 0b01x means we are testing the state of the Bool flag. 0b1xx is comparing two numbers. The Least Significant being the accumulator value and the next bit being the tested number. You could imagine the mathematical comparision symbols between these bits.
0b1-10 --> test number is greater, 0b1-01 --> accumulator is greater
0b1-11 --> means they are equal, thus 0b1-00 must mean they are different.
Under a similar train of thinking, each argument is a segregated byte and a simple number, thus not much to get wrong there.
8 - The microcode still needs to be written by machine. You are screwed if you have an HexVex computer with cleared ROMs. Any Microcode value not in use (usually due an illegal combination of instructions) will be loaded with the "Skip Instruction" pattern. It's conceivable that these values can be hacked for custom opcodes or features. The patterns are the following:
[Fill in another day]
9 – The system interruption mechanism works by dedicating the last addresses of the Program Memory to ngoto opcodes which lead the system to whatever program pointer the relevant code is found. When the Interrupt Handling hardware is triggered, it causes a jump to one of the last addresses. The attribution between specific interrupt and associated program address is hardwired. But the pointer where these interrupts lead to, after running their ngoto instructions can be freely defined in software and they are interpreted no different from user defined labels.
10 – The standard GPIO devices when in output mode will behave pretty much like any plain register. When writing into them, the register stores the value. When reading, the value is taken from the register. When the GPIO is in Input mode, the writing will hopelessly be registered, while reading will be take whatever value comes from the external interface. At the same time, the internal register will be set to that external value too, so it’s possible to switch the device to output mode and the last externally read value will still be accessible. Otherwise register in input mode could be thought as a write-only device. It must also be noted the quirk that it’s possible to write to an input-mode device and if no read is done afterwards, the written number will still be present.
11 – The choice of setup pattern’s second bit to be «0» for output mode and «1» for input mode is deliberate, given that the symbol for these numbers looks similar to the letters “O” and “I”. The choice of «0» for the first bit to be the “toggle mode” action is so that you can either use poke or tell for the same effect. So the setup pattern doesn’t matter if you just want to toggle the mode.

# History and Plans for HexVexNxt
Logic gates
Shenzhen I/O
Watchdog.
Internal Analogue I/O register.
Mechanism to synchronize with real-time seconds.
Expandable program memory and pointer counter.
Self-programming facilities.
Type 2 assembly.
High level language.
# Interesting Programs to try out
## Division:
With the lack of floating point capability in HexVex, it isn’t possible to have a number division ALU module. But you can emulate it in software. A basic version would calculate the integer quotient approximation and modulus. A more advanced version could calculate floating points by successive approximations.
## Integration:
Try writing a program which requires mathematical integration. Like finding out the velocity of a pneumatic piston, predict the time constant of a capacitor filter, the ballistic trajectory of a missile or the velocity of an antipodal train travelling through the centre of the Earth.
## Trigonometry:
Trigonometry is tri-cky! Maybe you can do a program to compute the sides of a triangle. Or better, the sine and cosine, which then you can output the result through analogue output and synthesize audio!
## Fast Fourier Transform:
If audio synthesis isn’t hard enough for you, maybe you’ll want to take analogue input instead and make a program to find the frequency components of any signal.
## Computer Virus:
A computer virus is a program that, much like a biological virus, uses the host (the program memory) to replicate itself, potentially spreading its own code to to other computers. If you add an EEPROM or a RAM as a peripheral device, could you make a program which writes the same code as itself to that?
## Graphical Display:
It is possible to have a peripheral device which is a pixel matrix where each pixel can be selected by two registers representing the horizontal and vertical coordinates for that pixel. This kind of display could work much like a RAM where you can set the values of each row of data individually and they’d persist while other values are being modified. In such way a primitive display for visual output is possible. The fact that each register is 8 bits allows a maximum resolution of 256 by 256 pixels. But with extra trickery it’s possible to have larger resolutions at the cost of extra computing cycles. Updating the display with the help of the Auxiliary Bus, using the Cache as intermediary bus management and poke for special writing, more complex displays or 16 bit (65536 pixels wide) resolutions!
## Videogames:
If you achieved to plug in a display, you might then be able to design a game of Tetris, Snake, Asteroids, Missile Command, Solitaire or Space Invaders. Video games are both the most computationally demanding applications and the hardest to code. They employ trignometric operations, timer, graphics and audio, all in tandem. This is a real challenge of your skills!
# Hardware for extra power
## Better Multiplication:
Algorithms to calculate multiplication of two numbers abound. Maybe you can make a better multiplication circuit from the default one. Better, faster, harder, stronger.
## Differential Engine:
One of the first and still most astounding computing devices was Charles Babbage’s Difference Engine. It was used to find the coefficients of polynomials by the method of differences and approximations he devised for use with only addition operations. Theoretically, this mathematical process can be used to approximate any arithmetical equation to an arbitrary degree. HexVex with a hardware implementation of the algorithm of this machine wouldn’t need any other ALU module!
## Numerical Decoders:
What if one of the devices connected to HexVex is a 7 segment display? To show the numbers properly you’d need a binary-to-7-segment conversion circuits for each digit... There must be a be a better way! An ALU module which takes a binary number and returns the display pattern is exactly the right thing.
Other types of decoding or encoding devices can also be useful. Some sensors send Gray Code, which must be converted to normal binary representation before being used as input for maths, for example.
You could also develop your own code system for cryptography purposes. Cryptography is much faster and safer in dedicated hardware implementations!
## Random Number Generators:
Talking about cryptography, a lot of it requires a random number to be unpredictable, thus truly safe. Videogames and simulation software also make a lot of use of random numbers. A computer by itself, using only basic arithmetic can’t generate true randomness in software only.